## Slide 1: Installing and Configuring Output Devices

## Slide 2
An output device is a device that sends data out of the computer and creates a tangible output.
Examples of output for the system are displaying information on the monitor, printing out a report, or even listening to the sound that the sound card puts through the speakers when playing your favorite computer games.

## Slide 3: Video Adapters
Also known as the video card, is the interface between the monitor and the computer and is responsible for converting the digital data from the computer into analog information.

## Slide 4: Basic role of video adapter
Data is sent to the video card via the expansion bus that the video card resides in.
The video chipset on the video card writes the data to memory located on the card.
After being stored in memory, the data is passed to the digital-to-analog converter (DAC), where it is converted from digital signals to analog signals that the monitor can understand.
The data is passed to the monitor, which then displays the data on the screen.

## Slide 5: Video Adapter

## Slide 6: Video standards
Monochrome Display Adapter (MDA): The MDA standard displays data in a text format with a single color — white text on the black screen. This standard is pretty much obsolete, but you may encounter an old server that still uses it.
Color Graphics Adapter (CGA): The CGA standard is the next step above MDA and supports four colors in a 320 x 200 resolution but supports only two colors with a resolution of 640 x 200. CGA video adapters were the first adapters to support color.
Enhanced Graphics Adapter (EGA): The next step after CGA is EGA, which is much improved over the CGA graphics standard. EGA supports 16 colors at 640 x 350 resolution.

## Slide 7: Video standards…
Video Graphics Array (VGA): VGA is a video graphics standard that allows for a resolution of 640 x 480 with 16 colors, but also supports 256 colors at lower resolutions.
Super VGA (SVGA): Super VGA supports 16 million colors at resolutions as high as 1280 x 1024 and is the graphics standard of today.

## Slide 8: Installing a video card
Installing any other card, you simply need to place the card into a supported bus
architecture, typically either PCI or AGP, and then load the driver.

## Slide 9: Steps
Power off and unplug the computer.
Open the case or side panel of the computer so that you can access the expansion slots.
If you are replacing a video card, take out the old one. If the old video card is integrated into the motherboard, you will not be able to remove it, but you may be able to disable it in CMOS.
If you are adding the first video card to the system, then remove the blanking plate for the AGP or PCI slot you wish to use.
Insert the card into the slot until it fits firmly.
Screw the video card’s plate into place to secure the card.
Place the cover back on the computer, plug it back in, and power it on

## Slide 10
When you power up the system, Plug and Play should kick in and detect the newly added device and either load a driver or prompt you for the driver.
After the driver is loaded, you will be able to configure the display settings.

## Slide 11: Using Your Monitor
After you install the video adapter, you then need to connect the monitor to the video adapter.

## Slide 12: Types of displays
Cathode Ray Tube (CRT): Cathode Ray Tube (CRT) monitors were popular for computing for many years and were also popular as television screens.
After receiving a signal from the video card, a CRT monitor displays the image by using an electron gun that shoots electrons at the phosphors covering the back of the screen, causing those areas of the screen to glow.
LCD: A Liquid Crystal Display (LCD) is a flat monitor type that has been used with laptops for many years and is now used for flat-screen desktop monitors.

## Slide 13: Types of displays…
Projector: Screen projectors are becoming popular both for home theater systems and in boardrooms.
When using a computer or laptop with a projector, the projector connects to the video adapter via a 15-pin video port

## Slide 14: Configuring your display settings
Choose Start➪Control Panel➪Appearance and Themes➪Display.
Click the Settings tab
From the Color Quality drop-down list, choose how many colors you want your display to support . 16-bit supports 65,536 colors, 24-bit supports 16 million colors. 32-bit supports over 16 million colors.
In the Screen Resolution section, move the slider to set the resolution of your monitor to the desired setting.
Click OK.
When asked if the display looks okay, click Yes.

## Slide 15
Read on Configuring multi-display support